PPM-java
Technical documentation
PH, 2017-01-13
# Introduction
According to an Article on Wikipedia[1], "a peak programme meter (PPM) is an instrument used in professional audio for indicating the level of an audio signal." It is different from a normal VU meter in that it has a very short rise time (integration time) and a long return time. This allows audio producers to continouusly monitor the peaks of a programme signal. ppm_java implements a PPM type II which has a rise time of 23 dB in 10 ms and a fall time of -24dB in 2800ms.
[1] https://en.wikipedia.org/wiki/Peak_programme_meter
The audio level maps to the meter scale as:
Input level [dB]		Meter mark
min	max	min	max
-130	-24	0	1
-24	-20	1	2
-20	-16	2	3
-16	-12	3	4
-12	-8	4	5
-8	-4	5	6
-4	0	6	7
0	...	7	7

## System requirements
ppm-java requires
- Java (Tested with Java 1.8.)
- JackD audio server (Tested with version 1.9.10)
Test setup was a Linux machine (Kubuntu 14); program hasn't been tested on other platforms.
# Running
ppm-java runs as a Jack client which means that there must be a running instance of JackD before starting ppm-java. Once both of them are running, ppm-java will find the running JackD server and register as a client. The ppm-java client can then connect to outputs of any other clients registered with JackD and watch the audio levels.
## Example session
If JackD isn't running, start it:
user@local:~$ /usr/bin/jackd -r -dalsa -dhw:0 -r44100 -p1024 -n3 -Xraw
Start ppm-java from the commandline. We'll run it with the graphical linear gauge:
user@local:~$ java -jar /path/to/ppm.jar -u guiLinear -l /var/log/ppm.log
This will bring up a horizontal linear gauge. If the meter is receiving audio data the gauge will show the current audio levels:
# Design and challenges
For the user this program has a very simple purpose: It just displays the level of a stereo signal using PPM II ballistics. The program should scale easily to implement new features. For example, the user might be interested in a history view to see the last minute of level measurements. Or, the meter could be used as a silence detector, sending an alarm event somewhere if the audio level falls below a threshold for a prolonged time. To aid scalability the program follows a modular design. Developing ppm-java posed several challenges:
- Good balance between scalability and fitness for the purpose. The challenge is to create a framework which is well suited for the task whilst being generic enough to accomodate further development.[2]
  [2] This is a hard balancing act - it's tempting to totally overengineer and create micromodules or to go the shortcut route and hack some contorted monolithic construction. Half a year later even the author won't have a clue what this thing does!
- Making two parallel activities with different priorities work together. On one side we have got a high priority activity (the JackD process), on the other side we've got a low priority activity (user interface updates). Both sides run independently of each other, i.e. in separate threads. We have to avoid priority inversion where the low priority thread (user interface updates) blocks the high priority thread (JackD).
- Minimizing data loss. The high priority JackD thread needs to work need for a protection against priority inversion brings up the possibility of data loss. For example we get data loss if the user interface thread blocks, whilst the JackD thread keeps pushing audio data. The challenge is to build in some mechanism that minimizes data loss.
- Keeping performance up. We need a framework which is able to process the audio data without much latency, so that updates on the meter happen almost immediately after the corresponding audio has come into the meter. There's always some latency with any audio application, but for a a metering solution the latency should be less than 25ms.
# Implementation
ppm-java is a jack client, i.e. it works with the Jack audio server. The program has to constantly update a graphical user interface as well. The main work is done in two different threads: The audio driver thread which receives the samples from the Jack server and the analysis and display engine which runs the GUI side of things.
The audio driver thread is time critical as it integrates with the Jack server. This means we cannot afford to have the audio driver run slow on us, as this would affect the Jack server and potentially the whole ecosystem of clients connected with the Jack server. The analysis and display engine (GUI side) not time critical - if it hangs for a few moments it's user annoying but at least it doesn't pull the entire Jack system down with it! For the program to run well we need to prevent priority inversion where the low priority thread (display engine) blocks the high priority thread (audio driver). We need to decouple the display engine from the audio driver in such a way that the audio driver won't get stuck (even if the display engine is frozen) and the display engine receives the audio data with minimal data loss.
Because of the need for decoupling we cannot send data directly from the audio driver to the display engine. The mechanism between both is a bank of atomic buffers (one per channel) which receives data from the audio driver and holds it ready for the display engine when it fetches the data. The atomic buffers act as a priority inversion barrier between the display engine and the audio driver.
## Audio driver (JJack)
ppm-java relies on the Jack audio server[3] as audio backend which runs in it's own process, jackd. All communication with Jack is encapsulated in the class ppm_java.backend.module.jackd.TAudioContext_JackD which relies on the JJack library[4] for the actual connection with Jack.
[3] http://www.jackaudio.org
[4] https://sourceforge.net/projects/jjack
JJack makes it easy to write Jack clients. Here's a client that receives audio from a port on the Jack server and prints peak sample values on the console (full program, see appendix 1, listing 1):

package ppm_java._dev.concept.trial.JJack;

import... /* Various imports */

/**
 * Loads the JJack driver, connects to a running instance of JackD and prints
 * the peak of every incoming frame to stdout.
 *
 * @author peter
 */
public class TDev_Trial_JJack_process_01 implements JJackAudioProcessor
{
    public static void main (String[] arge) {/* Setup stuff... */}

    private int fIFrame = 0;
    public TDev_Trial_JJack_process_01 ()
    {
        fIFrame = 0;
    }

    public void process (JJackAudioEvent e)
    {
        FloatBuffer inBuf;
        int nSamples;
        int i;
        float s;
        float sRect;
        float peak;

        fIFrame++;
        inBuf = e.getInput (0);
        nSamples = inBuf.limit ();
        peak = 0;
        for (i = 0; i < nSamples; i++)
        {
        /* Get next sample. */
        s = inBuf.get (i);

        /* Rectify (i.e. mirror a negative sample to it's positive opposite). */
        sRect = (s < 0) ? -s : s;

        /* Determine peak value. */
        peak = (sRect > peak) ? sRect : peak;
        }
        System.out.println ("Frame: " + fIFrame + "; Peak value (abs): " + peak + ".");
    }
}

The central piece of this code is the method process(JJackAudioEvent e). The method receives one parameter of type JJackAudioEvent (provided by JJack) which contains everything needed to extract and push audio data from/to the Jack server. All the client's sample processing is done in the process(...) method.
The Jack server (via the JJack bridge) calls this method in an endless cycle (about 20 .. 50 times per second) until the program ends.
Here's the program output:
1. native jjack library loaded using system library path
2. natively registering jack client "JJack"
3. jack_client_new: deprecated
4. using 2 input ports, 2 output ports
5. Frame: 1; Peak value (abs): 0.0.
6. Frame: 2; Peak value (abs): 0.0.
7. Frame: 3; Peak value (abs): 0.0.
8. Frame: 4; Peak value (abs): 0.042320143.
9. Frame: 5; Peak value (abs): 0.036235876.
10. Frame: 6; Peak value (abs): 0.038238987.
11. Frame: 7; Peak value (abs): 0.038017016.
12. Frame: 8; Peak value (abs): 0.04076365.
13. Frame: 9; Peak value (abs): 0.022242684.
14. Frame: 10; Peak value (abs): 0.022647541.
In ppm-java we cannot push the data directly to the display engine. The engine could have a blockage whilst it receives data which would result in the audio driver being stuck in the process(...) method. To prevent this priority inversion from happening we push the audio data to a bank of atomic buffers (one per audio channel) from where the display engine will fetch it. The atomic buffers are designed to never block the audio driver thread. This way we decouple the time critical audio driver thread from the low priority display engine thread. The display engine might still get stuck - but now the only consequence would be lost data. The audio driver will continue to work, even if the display engine freezes up.
## GUI side (low priority) [current_edit]
The analysis and display engine main work of ppm-java is done inside the low priority display thread.
## Atomic buffer [TODO]
We could have made our program very short and include all code inside the process(...) method:

public void process (JJackAudioEvent e)
{
    /* for each input channel... */
    /* find peak in e.getInput() */
    /* convert peak value to dB */
    /* interpolate to PPM ballistics */
    /* update GUI */
}

Whilst this is a really nice shortcut, it's not a good idea to implement it! The process(...) method is time critical, and we would have put a lot of non-time-critical code into the time critical section that way - which could well choke the Jack server.if our non-time-critical code gets stuck somewhere. Furthermore we would update the GUI with the frequency of Jack calling the process(...) method which might be too slow for a smooth visual appearance.
Therefore we need a solution where we decouple the time critical section (in process(...)) from all the other activity of our program and place all the GUI updates into code that runs in another thread, separately from the Jack server process.
The central piece to the solution is the atomic buffer, implemented as class (ppm_java.util.storage.TAtomicBuffer). This class stores the audio samples coming from the input side and releases them to the GUI side when requested. The buffer is atomic in the sense that one thread at a time can read/write data to/from the buffer.
## Class hierarchy [TODO]
# Roadmap
- Finish documentation (est. one week).
- True peak capabilities. So far, we just take the highest absolute sample value per GUI cycle and use that for the display. However, in reality most peaks fall between peaks on the actual waveform. This means our meter does not display the waveform peaks but only the sample peaks, resulting in an underread of typically 3dB. A truepeak module is needed to reduce the underread. We would design the truepeak module according to the recommended algorithm in BS.1770-4[5] (est one week).
  [5] BS.1770-4, Annex 2. https://www.itu.int/dms_pubrec/itu-r/rec/bs/R-REC-BS.1770-4-201510-I!!PDF-E.pdf
- Port to C++/QT. The ppm-java program is a proof of concept. And it was simply easier to do the design in Java (e.g. we don't have to keep track of header files). Once the design has matured, it should be fairly straight forward to port the program to C++, using the QT toolkit and other support libraries (est. four weeks).
# Appendices
## App. 1: Example listings
### Listing 1:

package ppm_java._dev.concept.trial.JJack;

import java.nio.FloatBuffer;
import de.gulden.framework.jjack.JJackAudioEvent;
import de.gulden.framework.jjack.JJackAudioProcessor;
import de.gulden.framework.jjack.JJackException;
import de.gulden.framework.jjack.JJackSystem;
import ppm_java.util.logging.TLogger;

/**
 * Loads the JJack driver, connects to a running instance of JackD and prints
 * the peak of every incoming frame to stdout.
 *
 * @author peter
 */
public class TDev_Trial_JJack_process_01 implements JJackAudioProcessor
{
    public static void main (String[] args)
    {
        TDev_Trial_JJack_process_01 processor;

        /* Setting up Jack client and terminator thread. */
        processor = new TDev_Trial_JJack_process_01 ();

        /* Connecting with the running instance of Jack */
        JJackSystem.setProcessor (processor);

        /* Terminator timer - must run in separate thread */
        new Thread ()
        {
        public void run ()
        {
        try
        {
        Thread.sleep (500);
        JJackSystem.shutdown ();
        }
        catch (JJackException | InterruptedException e)
        {
        e.printStackTrace();
        }
        System.exit (1);
        }
        }.start ();
    }

    private int fIFrame;

    public TDev_Trial_JJack_process_01 ()
    {
        fIFrame = 0;
    }

    /**
     * The process callback. Called by the Jack server via the JJack bridge. Time critical!
     */
    @Override
    public void process (JJackAudioEvent e)
    {
        FloatBuffer inBuf;
        int nSamples;
        int i;
        float s;
        float sRect;
        float peak;

        fIFrame++;
        inBuf = e.getInput (0);
        nSamples = inBuf.limit ();
        peak = 0;
        for (i = 0; i < nSamples; i++)
        {
        /* Get next sample. */
        s = inBuf.get (i);

        /* Rectify (i.e. mirror a negative sample to it's positive opposite). */
        sRect = (s < 0) ? -s : s;

        /* Determine peak value. */
        peak = (sRect > peak) ? sRect : peak;
        }
        System.out.println ("Frame: " + fIFrame + "; Peak value (abs): " + peak + ".");
    }
}

## Glossary
Priority inversion
In computer science, priority inversion is a problematic scenario in scheduling in which a high priority task is indirectly preempted by a lower priority task effectively "inverting" the relative priorities of the two tasks.
This violates the priority model that high priority tasks can only be prevented from running by higher priority tasks and briefly by low priority tasks which will quickly complete their use of a resource shared by the high and low priority tasks.
https://en.wikipedia.org/wiki/Priority_inversion
# License
A program to display audio levels using PPM ballistics.
Copyright (C) 2017 Peter Hoppe
This program is free software: you can redistribute it and/or modify it under the terms of the GNU General Public License as published by the Free Software Foundation, either version 3 of the License, or (at your option) any later version.
This program is distributed in the hope that it will be useful, but WITHOUT ANY WARRANTY; without even the implied warranty of MERCHANTABILITY or FITNESS FOR A PARTICULAR PURPOSE. See the GNU General Public License for more details.
You should have received a copy of the GNU General Public License along with this program. If not, see <http://www.gnu.org/licenses/>.