PPM-java
Technical documentation
PH, 2017-01-13
# This guide has been written by a dude who isn't a technical writer.
# Written with thanks to my better half who patiently endured my long computer sessions!
# Introduction
According to an Article on Wikipedia[1], "a peak programme meter (PPM) is an instrument used in professional audio for indicating the level of an audio signal." It is different from a normal VU meter in that it has a very short rise time (integration time) and a long return time. This allows audio producers to continouusly monitor the peaks of a programme signal. ppm_java implements a PPM type II which has a rise time of 23 dB in 10 ms and a fall time of -24dB in 2800ms.
[1] https://en.wikipedia.org/wiki/Peak_programme_meter
The audio level maps to the meter scale as follows:
Input level [dB]		Meter mark
min	max	min	max
-130	-24	0	1
-24	-20	1	2
-20	-16	2	3
-16	-12	3	4
-12	-8	4	5
-8	-4	5	6
-4	0	6	7
0	...	7	7

# Running
## System requirements
ppm-java requires
- Java (Tested with Java 1.8.)
- Jack audio server[2] (Tested with version 1.9.10)
  [2] The Jack server connects audio programs and hardware so they can communicate with each other. See http://www.jackaudio.org
Test setup was a Linux machine (Kubuntu 14); program hasn't been tested on other platforms.
## Example session
If JackD isn't running, start it:
user@local:~$ /usr/bin/jackd -r -dalsa -dhw:0 -r44100 -p1024 -n3 -Xraw
Start ppm-java from the commandline. We'll run it with the graphical linear gauge frontend:
user@local:~$ java -jar /path/to/ppm.jar -u guiLinear -l /var/log/ppm.log
This will bring up a horizontal linear gauge. If the meter is receiving audio data the gauge will show the current audio levels:
# ­Implementation
## Design overview
ppm-java runs as a Jack client. Jack runs in it's own process, jackd. This means that there must be a running instance of jackd before starting ppm-java. Once both of them are running, ppm-java will find the running jackd server and register as a client. The user can then connect ppm-java to outputs of any other clients registered with JackD and display the audio levels on a frontend.
Through the Jack audio server, ppm-java receives audio data from attached hardware or from other Jack compatible programs. All communication with Jack is encapsulated in the module TAudioContext_JackD which relies on the JJack library[3] for the actual connection with Jack.
[3] https://sourceforge.net/projects/jjack
The program is designed in a modular fashion which requires a framework supporting the modular nature. This modular arrangement increases complexity initially, but the makes the design much more flexible. For example, it was easy to accomodate a special case for the consoleText frontend in that we don't include PPM ballistics. Also, a modular design aids development of new features. For example, the user might be interested in a history view to see the last minute of level measurements. Or, the meter could be used as a silence detector, sending an alarm event somewhere if the audio level falls below a threshold for a prolonged time.
When running, ppm-java continouusly receives chunks of audio samples from the Jack server, and, for each chunk,
- computes the absolute peak value,
- converts it from raw sample values to decibels,
- applies a stepping integrator (PPM ballistics),
- and displays the result on a frontend.
Two activites are happening here: On the one hand, Jack delivers sample chunks, and, on the other hand, the program updates a display. These are two distinct activities, and both run in separate threads. The Jack side of things is handled by the audio driver thread, and everything else runs within the display engine thread. Connecting both sides together presents an interesting challenge as we link a high priority thread (audio driver, time critical) and a low priority thread (display engine, may hang sometimes).
The audio driver thread is time critical as it integrates with the Jack server. This means we cannot afford to have the audio driver run slow on us, as this would affect the Jack server and potentially the whole ecosystem of clients connected with the Jack server[4]. The display engine (GUI side) isn't time critical - if it hangs for a few moments it's user annoying but at least it doesn't pull the entire Jack system down with it! We need to prevent priority inversion where the low priority thread (display engine) blocks the high priority thread (audio driver). We have to decouple the display engine from the audio driver in such a way that the audio driver won't get stuck (even if the display engine is frozen) whilst the display engine receives the audio data with minimal data loss.
[4] Might not be as dramatic (Jack has got protection measures against slow clients), but it isn't prudent to assume external safety. No hard feelings and I do respect the Jack developers, but for our application development the safest assumption is the worst case presumption: Jack's a sensitive soul and has a crisis with slow clients. Let's have a well behaved client, not a liability!
Because of the need for decoupling we cannot send data directly from the audio driver to the display engine. Instead we use a bank of special buffers (one per channel) which receives data from the audio driver and holds it ready for the display engine when it fetches the data. The buffers are designed such that setting and fetching are atomic, i.e. only one thread a time can read/write data to the buffer (That's why we call them 'atomic buffers'). The bank of buffers acts as a priority inversion barrier between the display engine and the audio driver.
## Challenges
- Good balance between scalability and fitness for the purpose. The challenge is to create a framework which is well suited for the task whilst being generic enough to accomodate further development[5].
  [5] This is a hard balancing act - it's tempting to totally overengineer and create micromodules or to go the shortcut route and hack some contorted monolithic construction. In both cases, half a year later even the author won't have a clue what this thing does!
- We have to protect against priority inversion where the low priority thread (display engine) blocks the high priority thread (audio driver).
- At the same time we have to minimize data loss between the audio driver and the display engine - as the protection will de-integrate them.
- We need to process the audio data without much latency, so that updates on the meter happen almost immediately after the corresponding audio has come into the meter. There's always some latency with any audio application, but for a a metering solution the latency should be less than 25ms.
# Multithreading
ppm-java makes extensive use of multithreading. As example, the atomic buffer (class TAtomicBuffer) stores the audio samples coming from the input side and releases them to the GUI side when requested. Setting data and fetching data is done by two different threads, at the same time. One thread constantly pushes data to the buffer, whilst the other thread constantly fetches it from the buffer. This is a classic producer/consumer scenario.
Without precautions, if multiple threads access the same object we can get surprising results. The following program has two theads simultaneously access a shared buffer. One thread pushes data, the other thread pops it[6]. No precautions are taken to make this program “multithread-proof”.
[6] Note that, in this program, push and pop just increment / decrement a counter. The point of the demo still holds.
Main program:

package ppm_java._dev.concept.example.multithread.unsafe;

public class TDev_Example_multithread_unsafe
{
    public static void main (String[] args)
    {
        TDev_Example_multithread_unsafe unsafeClient;

        unsafeClient = new TDev_Example_multithread_unsafe ();
        unsafeClient.start ();
    }

    private TThreadConsumer fConsumer;
    private TThreadProducer fProducer;
    private int fValue;

    /**
     *
     */
    public TDev_Example_multithread_unsafe ()
    {
        fConsumer = new TThreadConsumer (this);
        fProducer = new TThreadProducer (this);
        fValue = 0;
    }

    public void start ()
    {
        fConsumer.start ();
        fProducer.start ();
    }

    public void Pop ()
    {
        System.out.println ("Entering Pop (). Number: " + fValue);
        if (fValue > 0)
        {
        fValue--;
        try {Thread.sleep (500);} catch (InterruptedException e) {}
        }
        System.out.println ("Exiting Pop (). Number: " + fValue);
    }

    public void Push ()
    {
        System.out.println ("Entering Push (). Number: " + fValue);
        if (fValue < 1)
        {
        fValue++;
        try {Thread.sleep (500);} catch (InterruptedException e) {}
        }
        System.out.println ("Exiting Push (). Number: " + fValue);
    }
}

Producer:

package ppm_java._dev.concept.example.multithread.unsafe;

class TThreadProducer extends Thread
{
    private TDev_Example_multithread_unsafe fHost;

    public TThreadProducer (TDev_Example_multithread_unsafe host)
    {
        fHost = host;
    }

    @Override
    public void run ()
    {
        int i;
        int delay;

        delay = 0;
        for (i = 1; i <= 10; i++)
        {
        fHost.Push ();
        delay += 10;
        try {Thread.sleep (delay);} catch (InterruptedException e) {}
        }
    }
}

Consumer:

package ppm_java._dev.concept.example.multithread.unsafe;

class TThreadConsumer extends Thread
{
    private TDev_Example_multithread_unsafe fHost;

    public TThreadConsumer (TDev_Example_multithread_unsafe host)
    {
        fHost = host;
    }

    @Override
    public void run ()
    {
        int i;
        int delay;

        delay = 200;
        for (i = 1; i <= 10; i++)
        {
        fHost.Pop ();
        delay -= 10;
        try {Thread.sleep (delay);} catch (InterruptedException e) {}
        }
    }
}

The output of the program shows that Push() and Pop() are executed at arbitrary times. The producer and consumer just tread on each other's toes. The result is messed up data.
1. Entering Push (). Number: 0
2. Entering Pop (). Number: 0 <--- Pop() should not be executed here.
3. Exiting Push (). Number: 0 <--- Number should be 1.
4. Exiting Pop (). Number: 0
5. Entering Push (). Number: 0
6. Entering Pop (). Number: 1
7. Exiting Push (). Number: 0
8. Entering Push (). Number: 0
## Thread cooperation primitives.
Since version 1.0 Java has support for multithreaded applications. Most notably, the language provides the synchronized keyword. This keyword allows us to make methods or code blocks thread-safe. The synchronized keyword creates a protected section of code that can only be entered by one thread a time. Such a section is called a critical section.
To make our previous example multithread proof we need to declare the main program's Push() and Pop() methods as synchronized.

    public synchronized void Pop ()
    {
        System.out.println ("Entering Pop (). Number: " + fValue);
        if (fValue > 0)
        {
        fValue--;
        try {Thread.sleep (500);} catch (InterruptedException e) {}
        }
        System.out.println ("Exiting Pop (). Number: " + fValue);
    }

    public synchronized void Push ()
    {
        System.out.println ("Entering Push (). Number: " + fValue);
        if (fValue < 1)
        {
        fValue++;
        try {Thread.sleep (500);} catch (InterruptedException e) {}
        }
        System.out.println ("Exiting Push (). Number: " + fValue);
    }

This creates order, as both threads politely wait for each other! Now, our data is correct:
1. Entering Pop (). Number: 0
2. Exiting Pop (). Number: 0
3. Entering Push (). Number: 0
4. Exiting Push (). Number: 1
5. Entering Pop (). Number: 1
6. Exiting Pop (). Number: 0
7. Entering Push (). Number: 0
8. Exiting Push (). Number: 1
9. Entering Pop (). Number: 1
10. Exiting Pop (). Number: 0
The synchronized keyword turns a method (or block of code) into a protected section. When a thread executes such a section then any other thread trying to execute the same section is suspended until the first thread has finished. This is the reason why the synchronization in our example program works. If the producer thread has entered the Push() method, and the consumer tries to enter the Pop() method before the producer has finished, then the consumer must wait until the producer has left the Push() method.
This mechanism operates object wide. Once a thread has acquired a protected section in an object, all other synchronized parts of that object are locked. The object is the lock; once it's acquired by a thread, no other thread can acquire it until the first thread has released the lock. In our example, both, Push() and Pop() are synchronized on the instance of TDev_Example_multithread_safe. This forces the producer and the consumer to wait for each other, ensuring data integrity.
### Wait problem

Synchronization means waiting. If one thread enters a synchronized section, all other threads have to wait (a thread trying will be suspended). This can block a thread for an uneccessarily long time. Here is an example which demonstrates the problem of the long wait:
Main program:

package ppm_java._dev.concept.example.multithread.wait;

public class THouse
{
    private static final int gkNumVisitors = 5;
    private static final long gkTimeAudience = 1000;

    public static void main (String[] args)
    {
        THouse house;

        house = new THouse ();
        house.GetMeSomeVisitors ();
    }

    private TVisitor[] fVisitors;

    public THouse ()
    {
        int i;

        fVisitors = new TVisitor [gkNumVisitors];
        for (i = 0; i < gkNumVisitors; i++)
        {
        fVisitors[i] = new TVisitor (this, i);
        }
    }

    public void GetMeSomeVisitors ()
    {
        int i;

        for (i = 0; i < gkNumVisitors; i++)
        {
        fVisitors[i].start ();
        }
    }

    public synchronized void Visit (int id)
    {
        try {Thread.sleep (gkTimeAudience);} catch (InterruptedException e) {}
    }
}

Visitor:

package ppm_java._dev.concept.example.multithread.wait;

class TVisitor extends Thread
{
    private THouse fHouse;
    private int fID;
    private String fPreamble;

    public TVisitor (THouse house, int id)
    {
        fHouse = house;
        fID = id;
        fPreamble = "Visitor #" + fID;
    }

    public void run ()
    {
        long t0;
        long t1;
        long dT;

        t0 = System.currentTimeMillis ();
        fHouse.Visit (fID);
        t1 = System.currentTimeMillis ();
        dT = t1 - t0;

        System.out.println (fPreamble + ": Had an audience! Time spent: " + dT + "ms.");
    }
}

A group of visitors would like to visit a house to have an audience with the home owner. The owner speaks to one visitor a time, for exactly one second. All others have to wait. Unfortunately, the output shows excessive waiting times for most visitors:
1. Visitor #0: Had an audience! Time spent: 1000ms. <--- Thread #0: Zero wait time!
2. Visitor #4: Had an audience! Time spent: 2000ms.
3. Visitor #3: Had an audience! Time spent: 3000ms.
4. Visitor #2: Had an audience! Time spent: 4000ms.
5. Visitor #1: Had an audience! Time spent: 5001ms. <--- Thread #1: Four seconds wait time!
The problem is the synchronization mechanism: When one thread acquires a lock, all other threads trying to acquire the same lock will be suspended until the lock is released. And that can be a long time waiting in suspense. For a realtime thread such as the audio driver in ppm-java, any wait is prohibitive.
### Wait free access
Since version 1.5 Java offers atomic variables in the package java.util.concurrent.atomic. Atomic variables are variables manipulated by one single processor instruction. As a side effect, this makes them inheritly thread-safe[7].
[7] With plain variables, thread safety is not guaranteed. For example, with a plain variable a simple assignment may need multiple processor instructions to complete which opens it up to data corruptions if manipulated by multiple threads simultaneously.
java.util.concurrent.atomic offers several types of atomic variables, but of special interest is the type java.util.concurrent.atomic.AtomicInteger, and especially it's method compareAndSet(). The proper signature of this method is

public final boolean compareAndSet (int expect, int update)

compareAndSet atomically sets the value to update if the current value equals expect. The method returns true if the value was successully changed and false if the value change failed. This method makes it useful to coordinate multiple threads without locking them up. Here is the visitor program again, this time using an AtomicInteger as coordination primitive:
Main program:

package ppm_java._dev.concept.example.multithread.waitfree;

import java.util.concurrent.atomic.AtomicInteger;

public class THouse
{
    private static final int gkNumVisitors = 5;
    private static final int gkTimeAudience = 1000;
    private static final int gkLocked = 1;
    private static final int gkUnlocked = 0;

    public static void main (String[] args)
    {
        THouse house;

        house = new THouse ();
        house.GetMeSomeVisitors ();
    }

    private AtomicInteger fState;
    private TVisitor[] fVisitors;

    public THouse ()
    {
        int i;

        fState = new AtomicInteger (gkUnlocked);
        fVisitors = new TVisitor [gkNumVisitors];
        for (i = 0; i < gkNumVisitors; i++)
        {
        fVisitors[i] = new TVisitor (this, i);
        }
    }

    public void GetMeSomeVisitors ()
    {
        int i;

        for (i = 0; i < gkNumVisitors; i++)
        {
        fVisitors[i].start ();
        }
    }

    public boolean Visit (int id)
    {
        boolean isSuccess;

        isSuccess = fState.compareAndSet (gkUnlocked, gkLocked);
        if (isSuccess)
        {
        try {Thread.sleep (gkTimeAudience);} catch (InterruptedException e) {}
        fState.getAndSet (gkUnlocked); // atomic setting
        }

        return isSuccess;
    }
}

Visitor:

package ppm_java._dev.concept.example.multithread.waitfree;

class TVisitor extends Thread
{
    private THouse fHouse;
    private int fID;
    private String fPreamble;

    public TVisitor (THouse house, int id)
    {
        fHouse = house;
        fID = id;
        fPreamble = "Visitor: " + fID;
    }

    public void run ()
    {
        long t0;
        long t1;
        long dT;
        long tTot;
        boolean isSuccess;

        tTot = 0;
        do
        {
        t0 = System.currentTimeMillis ();
        isSuccess = fHouse.Visit (fID); // Costs next to no time if fHouse is busy, i.e. no suspending!
        t1 = System.currentTimeMillis ();
        dT = t1 - t0;
        tTot += dT;
        if (isSuccess)
        {
        System.out.println (fPreamble + ": Had an audience! Time spent (total): " + tTot + "ms.");
        }
        else
        {
        // Couldn't get an audience this time. At least, my thread is not
        // suspended. I'll go and do something else and try again later.
        try {Thread.sleep (500);} catch (InterruptedException e) {}
        }
        }
        while (! isSuccess);
    }
}

The output shows that there's a lot less waiting than when using synchronized. Now, each visitor spends zero seconds wait time[8]:
[8] It may be confusing to you that it says “zero seconds of wait time” whilst the visitor thread does a Thread.sleep(500) when the isSuccess flag is false. Isn't Thread.sleep() a wait as well? In this context, it isn't! Because that sleep is not enforced from outside (via the synchronized mechanism), but chosen by the thread! Instead of sleeping the visitor could have done some other tasks, e.g. going for a walk, doing some shopping,... in the wait-free scenario it's up to the visitor thread what it does whilst waiting for the audience. With synchronized the sleep is enforced upon the visitor, i.e. the receptionist knocks him out.
1. Visitor: 1: Had an audience! Time spent (total): 1000ms.
2. Visitor: 0: Had an audience! Time spent (total): 1000ms.
3. Visitor: 2: Had an audience! Time spent (total): 1000ms.
4. Visitor: 3: Had an audience! Time spent (total): 1001ms.
5. Visitor: 4: Had an audience! Time spent (total): 1000ms.
The advantage of this way of thread coordination is that no thread ever gets suspended. All threads will continue to work, also those which unsuccessfully tried to enter a critical section. This is mandatory for time critical threads (such as the one running the audio driver), as they will never freeze.
Besides, some sources say that synchronization is much more expensive than atomic variables as the JVM does a lot of work in the background to operate it[9] whilst atomic variables are lightweight. Therefore, atomic variables incur less of a performance penalty than the synchronization primitive.
[9] https://www.ibm.com/developerworks/library/j-threads1 http://baptiste-wicht.com/posts/2010/09/java-concurrency-atomic-variables.html
To confirm that this thread coordination primitive really works, here is the initial producer-consumer scenario revisited, this time without synchronized methods, but using an AtomicInteger as lock[10]:
[10] It's on purpose that we don't use the AtomicInteger for the fValue field as the intend is to show that an AtomicInteger can be used as a lock to make the program thread-safe.
Main program:

package ppm_java._dev.concept.example.multithread.waitfree_testsafe;

import java.util.concurrent.atomic.AtomicInteger;

public class TDev_Example_multithread_waitfree_safe
{
    private static final int gkLocked = 1;
    private static final int gkUnlocked = 0;

    public static void main (String[] args)
    {
        TDev_Example_multithread_waitfree_safe unsafeClient;

        unsafeClient = new TDev_Example_multithread_waitfree_safe ();
        unsafeClient.start ();
    }

    private AtomicInteger fState;
    private TThreadConsumer fConsumer;
    private TThreadProducer fProducer;
    private int fValue;

    public TDev_Example_multithread_waitfree_safe ()
    {
        fConsumer = new TThreadConsumer (this);
        fProducer = new TThreadProducer (this);
        fValue = 0;
        fState = new AtomicInteger (gkUnlocked);
    }

    public void start ()
    {
        fConsumer.start ();
        fProducer.start ();
    }

    public boolean Pop ()
    {
        boolean success;

        success = fState.compareAndSet (gkUnlocked, gkLocked);
        if (success)
        {
        System.out.println ("Entering Pop (). Number: " + fValue);
        if (fValue > 0)
        {
        fValue--;
        try {Thread.sleep (500);} catch (InterruptedException e) {}
        }
        System.out.println (" Exiting Pop (). Number: " + fValue);
        fState.getAndSet (gkUnlocked);
        }

        return success;
    }

    public boolean Push ()
    {
        boolean success;

        success = fState.compareAndSet (gkUnlocked, gkLocked);
        if (success)
        {
        System.out.println ("Entering Push (). Number: " + fValue);
        if (fValue < 1)
        {
        fValue++;
        try {Thread.sleep (500);} catch (InterruptedException e) {}
        }
        System.out.println (" Exiting Push (). Number: " + fValue);
        fState.getAndSet (gkUnlocked);
        }

        return success;
    }
}

Producer:

package ppm_java._dev.concept.example.multithread.waitfree_testsafe;

/**
 * @author peter
 */
class TThreadProducer extends Thread
{
    private TDev_Example_multithread_waitfree_safe fHost;

    /**
     *
     */
    public TThreadProducer (TDev_Example_multithread_waitfree_safe host)
    {
        fHost = host;
    }

    @Override
    public void run ()
    {
        int i;
        int delay;
        boolean success;

        delay = 0;
        for (i = 1; i <= 10; i++)
        {
        delay += 10;
        do
        {
        success = fHost.Push ();
        try {Thread.sleep (delay);} catch (InterruptedException e) {}
        } while (! success);
        }

        System.out.println ("Producer finished!");
    }
}

Consumer:

package ppm_java._dev.concept.example.multithread.waitfree_testsafe;

/**
 * @author peter
 */
class TThreadConsumer extends Thread
{
    private TDev_Example_multithread_waitfree_safe fHost;

    /**
     *
     */
    public TThreadConsumer (TDev_Example_multithread_waitfree_safe host)
    {
        fHost = host;
    }

    @Override
    public void run ()
    {
        int i;
        int delay;
        boolean success;

        delay = 200;
        for (i = 1; i <= 10; i++)
        {
        delay -= 10;
        do
        {
        success = fHost.Pop ();
        try {Thread.sleep (delay);} catch (InterruptedException e) {}
        } while (! success);
        }

        System.out.println ("Consumer finished!");
    }
}

The program output shows two well behaved threads:
1. Entering Pop (). Number: 0
2. Exiting Pop (). Number: 0
3. Entering Push (). Number: 0
4. Exiting Push (). Number: 1
5. Entering Push (). Number: 1
6. Exiting Push (). Number: 1
7. Entering Push (). Number: 1
8. Exiting Push (). Number: 1
9. Entering Pop (). Number: 1
10. Exiting Pop (). Number: 0
11. Entering Push (). Number: 0
12. Exiting Push (). Number: 1
13. Entering Pop (). Number: 1
14. Exiting Pop (). Number: 0
15. Entering Push (). Number: 0
16. Exiting Push (). Number: 1
17. Entering Push (). Number: 1
18. Exiting Push (). Number: 1
19. Entering Push (). Number: 1
20. Exiting Push (). Number: 1
21. Entering Pop (). Number: 1
22. Exiting Pop (). Number: 0
23. Entering Push (). Number: 0
24. Exiting Push (). Number: 1
25. Entering Pop (). Number: 1
26. Exiting Pop (). Number: 0
27. Entering Push (). Number: 0
28. Exiting Push (). Number: 1
29. Entering Pop (). Number: 1
30. Exiting Pop (). Number: 0
31. Entering Push (). Number: 0
32. Exiting Push (). Number: 1
33. Entering Pop (). Number: 1
34. Producer finished!
35. Exiting Pop (). Number: 0
36. Entering Pop (). Number: 0
37. Exiting Pop (). Number: 0
38. Entering Pop (). Number: 0
39. Exiting Pop (). Number: 0
40. Entering Pop (). Number: 0
41. Exiting Pop (). Number: 0
42. Consumer finished!
In Summary: How to replace synchronized with a functionally equivalent wait-free lock[11]:
[11] You'll notice that the wait-free code is longer, but that's the price for the new wait-freedom!
Synchronized	Wait-free lock
Threadsafe part: / public class X / { / public X () / { / } / public synchronized void Do_Threadsafe_thing () / { / /* The payload */ / Do_Work (); / } / } / 0.30 cm	Threadsafe part: / import java.util.concurrent.atomic.AtomicInteger; / public class X / { / private AtomicInteger fState; / public X () / { / fState = new AtomicInteger (0); / } / public boolean Do_Threadsafe_thing () / { / boolean success; / /* Lockdown if unlocked */ / success = fState.compareAndSet (0, 1); / if (success) / { / /* The payload */ / Do_Work (); / /* Unlock critical section */ / fState.getAndSet (0); / } / /* Tell client thread whether work done */ / return success; / } / }
Thread using the threadsafe method: / public class Y extends Thread / { / private X fSpecimen; / public void run () / { / fSpeciment.Do_Threadsafe_Thing (); / } / }	Thread using the threadsafe method: / public class Y extends Thread / { / private X fSpecimen; / public void run () / { / boolean success; / do / { / success = fSpecimen.Do_Threadsafe_Thing(); / Do_other_Stuff_whilst_X_is_locked(); / try / { /* Thread puts itself to sleep / so that we don't get a / runaway thread freezing the / machine. */ / Thread.sleep (yieldTime); / } / catch (InterruptedException e) / { / } / } while (! success); / } / }

# Special constructs
## Atomic buffer
ppm-java connects a high priority thread (the audio driver) with a low priority thread (the display engine). The high priority driver is integrated with a realtime application (jackd) and must not be slowed down. The low priority thread operates a display, and can afford the occasional slowdown. We have a constant flow of audio data from the audio driver to the display engine. We need a connection that passes the data on to the display engine without slowing down the audio driver. The connecting piece is a bank of atomic buffers (ppm_java.util.storage.TAtomicBuffer), one buffer per audio channel.
The atomic buffer is designed for thread safety and data safety: The audio driver and the display engine won't freeze each other (no priority inversion) and data is deep copied before it reaches the consumer thread.
### Thread safety
The buffer uses the mechanisms described in chapter 4 (Multithreading) to provide thread coordination between the producer (audio driver) and the consumer (display engine). The thread coordination is wait-free for the high priority thread, and classically locking for the low priority thread (using a spin lock)[12].
[12] The spin locking shouldn't be a problem, because when the high priority thread acquires the critical section it spends very little time in it. It does very little work there, basically another method call followed by an if-statement and an assignment.
### Data safety
Due to the inner workings of the JJack library the audio frames are delivered as objects of type java.nio.FloatBuffer. If we passed these objects directly on to the consumer then any change done on the consumer side would be immediately mirrored on the producer side with potential side effects right up to the running jackd server[13]. That's why we perform a deep copy of the incoming FloatBuffer objects before passing them on to the consumer. This way, the consumer gets a copy and can change the data at will as it won't affect the producer.
[13] Might not be as dramatic, but it's safest to make the worst-case assumption.
As a downside, this introduces a performance penalty, as copying costs time. To protect the high priority thread from this penalty we use a copy policy which determines when the data will be copied[14]. This enables us to shift the extra copy work to the lower priority thread[15]. We have three possible copy policies (but the third one is very risky and should be used very sparingly!):
[14] Policy set via parameter copyPolicy to the TAtomicBuffer constructor.
[15] This brings it close to the “copy-on-write” technique.
- kCopyOnSet	Atomic buffer will copy when the producer sets the data. Use
  this policy when the producer is the low priority thread. This is the setting
  used with the default constructor.
- kCopyOnGet	Atomic buffer will copy when the consumer fetches (gets) the data. Use
  this policy when the consumer is the low priority thread.
- kNoCopy	Data won't be copied, but we pass on the original FloatBuffer
  objects.
  This policy is necessary in rare situations to prevent unnecessary
  multiple copying of data frames (e.g. when data is passed from one
  module to another). kNoCopy should be used very sparingly and
  carefully as it's a very risky option!
### Contention
The atomic buffer introduces a level of separation between the producer and consumer. For ppm‑java, this means the audio driver and the display engine are less tightly integrated. Whilst it makes both sides more independent of each other it brings with it some level of contention which manifests itself as buffer overuns, buffer underruns and dropped data.
In ppm-java contention issues arise because the audio driver delivers sample chunks at one frequency and the display engine updates the display at another frequency[16]. As result, both sides run with different schedules which will inevitably lead to conflicts.
[16] It would be bad design to fix-bind the GUI update frequency to the Jack update frequency. Saying that - we do employ a compensation scheme where we change the GUI update frequency until buffer underruns and Buffer overruns are minimized.
- For the audio driver, the update frequency depends on the sample rate and the size[17] of audio frames delivered. For example, if the sample rate is 44100 samples/sec and the frame size is 1024 samples per frame jackd will deliver a new frame every 1024 / 44100 s ≈ 20 ms.
  [17] Frame size depends on the running jackd instance, and that depends on how jackd was started (jackd commandline switch -p)
- For the display engine, the update frequency is initially 30 display updates per second[18].
  [18] Tthis will be modified by the contention compensation
During a ppm-java session we encounter three types of contention issues, each of which are indicated by an appropriate counter increment:
- Buffer overrun. This happens when the producer (audio driver) pushes data onto the buffer whilst uncollected stored data is still loitering in the buffer. If that happens the atomic buffer will increment an overrun counter.
- Buffer underrun. This happens when the consumer tries to collect data from the buffer whilst it's still empty, i.e. the producer hasn't pushed any data onto the buffer yet. If that happens the atomic buffer will increment an underrun counter.
- Thread contention. This happens when both, producer and consumer, try to access the critical data at the same time. If that happens the atomic buffer will increment a contention counter. In practice, this should be rare - but if it's not then it means that both, producer and consumer, are too aggressively competing over the atomic buffer.
All of these three contention types are revealed through the three counters which are exposed to clients through ppm-java's, statistics API. Clients can use the resp. counter values to mitigate over/underruns. Inside the buffer we use the following strategy to resolve contentions[19]:
[19] That's just the immediate dealing with a contention on the TAtomicBuffer side - the client has to still do additional steps to reduce contentions over time.
Overrun.
1. Let producer set the new data, discarding stale data[20].
  [20] New data always takes priority over old data. Therefore we simply drop any uncollected data.
2. Increment overrun counter.
Underrun.
1. Return new empty FloatBuffer or null[21] to the consumer.
  [21] Depending on the ifInvalidPolicy.
2. Increment underrun counter.
Thread contention.
Skip any data setting or getting, i.e.
- For the producer, drop the new data.
- For the consumer, return new empty FloatBuffer or null[22].
  [22] ditto
Increment thread contention counter.
We haven't mentioned another policy: The ifInvalidPolicy[23]. This policy determines what will be returned to the consumer in case of an underrun or thread contention. This policy is there purely for the benefit of the consumer. The following policies are possible:
[23] Set via parameter ifInvalidPolicy to the TAtomicBuffer constructor.
- kReturnNull. In case of contention, return null to the consumer. This makes consumer code a bit easier, as it's simpler to query for for null than to query whether a FloatBuffer is empty.
- kReturnEmpty. In case of contention, return an empty FloatBuffer to the consumer. There are situations where it's better to return a FloatBuffer to a consumer at all times, but never null, e.g. if a returned null causes a NullpointerException. That's why we provide the opportunity to return an empty FloatBuffer.
The TAtomicBuffer class could be changed to take other data items (e.g. arrays, ArrayLists, ...). It could be turned into a generic class, but this will need some thought as to the API of the stored objects - any stored object would need to support deep copying.
### JJack integration
We already use a dedicated library[24] to connect to the running jackd instance. At first glance it seems overkill to provide a wrapper class around that library. However and in general, it's better to contain an external API in one place than having it spill over into multiple places in this project. This makes future developments easier as it's straight forward to accomodate changes to the library's API or switch to a different library entirely[25].
[24] JJack
[25] JJack has come into its years. Currently, the last update on Sourceforge was 2014, and the latest version was uploaded in 2007. It still works, but for how long? Good enough for a concept application, though.
JJack makes it easy to write Jack clients. Here's a client that receives audio from a port on the Jack server and prints peak sample values on the console (full program, see appendix 1, listing 1):

package ppm_java._dev.concept.trial.JJack;

import... /* Various imports */

/**
 * Loads the JJack driver, connects to a running instance of JackD and prints
 * the peak of every incoming frame to stdout.
 *
 * @author peter
 */
public class TDev_Trial_JJack_process_01 implements JJackAudioProcessor
{
    public static void main (String[] arge) {/* Setup stuff... */}

    private int fIFrame = 0;
    public TDev_Trial_JJack_process_01 ()
    {
        fIFrame = 0;
    }

    public void process (JJackAudioEvent e)
    {
        FloatBuffer inBuf;
        int nSamples;
        int i;
        float s;
        float sRect;
        float peak;

        fIFrame++;
        inBuf = e.getInput (0);
        nSamples = inBuf.limit ();
        peak = 0;
        for (i = 0; i < nSamples; i++)
        {
        /* Get next sample. */
        s = inBuf.get (i);

        /* Rectify (i.e. mirror a negative sample to it's positive opposite). */
        sRect = (s < 0) ? -s : s;

        /* Determine peak value. */
        peak = (sRect > peak) ? sRect : peak;
        }
        System.out.println ("Frame: " + fIFrame + "; Peak value (abs): " + peak + ".");
    }
}

The central piece of this code is the method process (JJackAudioEvent e). The method receives one parameter of type JJackAudioEvent (provided by JJack) which contains everything needed to extract and push audio data from/to the Jack server. The method does all the client's sample processing. The Jack server (via the JJack bridge) calls this method in an endless cycle (several times per second) until the program ends. It's called as part of a thread running within jackd. This makes the process method a part of the running jackd instance. It also means that the execution of this method is time critical, i.e. a call to process(...) method must be guaranteed to complete in a fixed time shorter than the cycle time of the jackd instance.
Here's the program output:
1. native jjack library loaded using system library path
2. natively registering jack client "JJack"
3. jack_client_new: deprecated
4. using 2 input ports, 2 output ports
5. Frame: 1; Peak value (abs): 0.0.
6. Frame: 2; Peak value (abs): 0.0.
7. Frame: 3; Peak value (abs): 0.0.
8. Frame: 4; Peak value (abs): 0.042320143.
9. Frame: 5; Peak value (abs): 0.036235876.
10. Frame: 6; Peak value (abs): 0.038238987.
11. Frame: 7; Peak value (abs): 0.038017016.
12. Frame: 8; Peak value (abs): 0.04076365.
13. Frame: 9; Peak value (abs): 0.022242684.
14. Frame: 10; Peak value (abs): 0.022647541.
In ppm-java we cannot push the data directly to the display engine. If the engine blocks whilst it receives data it would result in the audio driver being stuck in the process(...) method , with unknown side effects for the running jackd instance (priority inversion). To prevent this from happening we push the audio data to a bank of atomic buffers (one per audio channel) from where the display engine will fetch it. The atomic buffers are designed to stream data from a high priority thread to a low priority thread without ever blocking the high priority thread. This way we decouple the time critical audio driver thread from the low priority display engine thread. The display engine might still get stuck - but now the only consequence would be lost data. The audio driver (i.e. the jack server) will continue to work, even if the display engine freezes up.
# Modules
This program uses a modular machinery. Various processor modules work together, each one performing a very specific sub task. All together they form a signal processing network. Network topology is set up at the start of the program and persists until it terminates.
Modules are connected to each other via endpoints. A module can have an arbitrary number of endpoints.
ppm-java supports two categories of endpoints - those that handle individual sample values and those that handle sample chunks. Endpoints can only connect to matching endpoints, e.g. an output that sends samples must connect to an input which receives samples.
Modules and endpoints are implemented as bespoke classes. They extend abstract base classes in the package ppm-java.typelib.
- A module class extends the base class VAudioProcessor.
- An output endpoint extends one of the classes VAudioPort_Output_Samples, VAudioPort_Output_Chunks_NeedsBuffer or VAudioPort_Output_Chunks_NoBuffer.
- An input endpoint extends one of the classes VAudioPort_Input_Samples, VAudioPort_Input_Chunks_Buffered or VAudioPort_Input_Chunks_Unbuffered.
Input and output endpoints must be connected to their matching counterpart.
Output endpoint type	Connects to input point type
VAudioPort_Output_Samples	VAudioPort_Input_Samples
VAudioPort_Output_Chunks_NeedsBuffer	VAudioPort_Input_Chunks_Buffered
VAudioPort_Output_Chunks_NoBuffer	VAudioPort_Input_Chunks_Unbuffered

Modules can be designed in many ways (the framework offers a lot of flexibility). However, to avoid chaos, this project keeps to the following practice:
- One package for each module class and supporting classes, at least the classes for the module and its endpoints. If the module supports the statistics API, then those supporting classes will be in there, too.
- The module's package contains one class for the module, named TNode{module_name}. Module classes derive from class ppm_java.typelib.VAudioProcessor.
- The module's package contains one class for the input endpoints, named {module_class_name}_Endpoint_In. Data between modules is always sent from output endpoints to input endpoints (rather than directly from module to module).
- The module's package contains one class for the output endpoints, named {module_class_name}_Endpoint_Out. Data between modules is always sent from output endpoints to input endpoints (rather than directly from module to module).
- The module's package contains one class for the statistics retrieval, named {module_class_name}_Stats. This class provides runtime statistics of the associated module. The module class must expose the associated statistics object to outside callers.
## Module reference
Class: TAudioContext_JackD / Package: ppm_java.backend.module.jackd / Purpose: The audio driver (backend). Acts as bridge between jackd and ppm-java.
Class: TNodePump / Package: ppm_java.backend.module.pump / Purpose: Data pump. Fetches audio data from the attached atomic buffer and passes it on to the next module, each time it receives a gkEventTimerTick. Compensates for buffer underruns / overruns.
Class: TNodePeakEstimator / Package: ppm_java.backend.module.peak_estimator / Purpose: Calculates the absolute peak value of a sample chunk. Being absolute, the value is always positive.
Class: TNodeConverterDb / Package: ppm_java.backend.module.converter_db / Purpose: Converts a sample (peak) value from raw level to dB. / Conversion according to y = 20 log10 (x) / where / x: normalized absolute sample value [Vnorm], 0 <= x <= 1 / y: sample value [dB]
Class: TNodeIntegrator_PPMBallistics / Package: ppm_java.front.module.integrator / Purpose: A stepping integrator to emulate PPM ballistics.
Class: VFrontEnd derivatives / Package: ppm_java.frontend.*.* / Purpose: The frontend used for the current session.

# Display engine
The main work of ppm-java is done inside the Display engine. This device takes the raw audio data and converts it to a stream of decibel values to be displayed on a front end or streamed via stdout to another application. With most frontends we include the PPM ballistics, streaming frontends omit PPM ballistics. As discussed elsewhere the analysis and display engine runs inside a low priority thread, but gets its input material from a high priority thread (audio driver) which requires extra measures to protect against priority inversion.
## Data loss compensation
The priority inversion protection comes at the price of data integrity. If the display engine does block (e.g. graphics takes longer than usual to do a refresh) then it will miss some of the data values coming from the audio driver. There isn't really any other way to resolve freeze-ups of the display engine than to simply drop past data and carry on with the current data. However, the display engine compensates for data loss, so it's kept at a minimum over time. The compensation is done inside the data pump module which sends gkTimerAdjustInterval events to the timer module during each display engine cycle. This increases or decreases the engine update frequency until the number of buffer underruns / overruns is minimized. In detail,
- if we detect underruns then there's too little data coming in from the audio driver. We need less display updates so we don't starve the display engine. Therefore we will instruct the timer to increase the update interval.
- if we detect overruns then there's too much data coming in from the audio driver. We need more updates to use all the data. Therefore we will instruct the timer to decrease the update interval.
Tests show that this scheme does resolve data loss very quickly. It's a bit unfortunate that this makes the data pump module more complex, but overall it's the simplest design.
# Frontends
Various frontends are available. Some offer graphical user interface, others work in text-only mode, i.e. in the console from which ppm-java has been started. Most of them include PPM ballistics in the display.
guiRadial	A PPM lookalike.
guiLinear	Horizontal linear bargraph.
consoleLinear	Horizontal linear bargraph on the console (text mode).
consoleText	Text stream to stdout. Data is presented in JSON format. This frontend is designed to stream audio level data to another application - e.g. via a pipe. / When ppm-java runs with this frontend, there will be no PPM ballistics, i.e. the peak values will be displayed directly, without integration.

# Session setup
ppm-java sets up the complete modular network right at the start of the program run. Network setup is done by the class ppm_java.backend.boot.TSetup. TSetup in turn uses the services of the class ppm_java.backend.TController which centralizes session setup and event routing. Everything pertaining to module creation and connection is done in the TController class, via a number of static methods. During the session each module can be addressed by a unique ID which we set during the setup phase. Modules, ports and frontends all inherit from the class ppm_java.typelib.VAudioProcessor and can hence be accessed by calling the method TController.GetObject (String id) with the unique ID of the object as parameter.
A network is built by
1. Creating modules,
2. Adding ports to each module,
3. Connecting ports for sample data,
4. Connecting modules to convey events.
Once built the network can be started.
## Creating modules
Before we can do anything with modules we need to create them. TController offers the methods
- Create_Module_X where X is the module to be created, e.g. for the TTimer module, we'd call the Create_Module_Timer method.
- Create_AudioContext for the audio driver, TAudioContext_JackD.
Each method takes one parameter, the unique ID under which the module can be accessed during the session.
## Adding ports
Once modules are created we can add ports to them. TController offers the methods
- Create_Port_In (String idModule, String idPort). Creates an input port on the module idModule. The port is named idPort.
- Create_Port_Out (String idModule, String idPort). Creates an output port on the module idModule. The port is named idPort.
## Data connections
With all modules and ports created we can connect ports together, so that samples can flow (that is, sample chunks and single samples). TController offers the method
Create_Connection_Data (String idFromPort, String idToPort)
This method creates a unidirectional audio data connection with port idFromPort as source and port idToPort as sink.
Note that ports must pair up correctly. You cannot connect a port which sends sample chunks to a port that receives single samples[26]. Such aberrations would throw an exception.
[26] This wouldn't make sense anyway
## Event connections
Within the network we use an event system to trigger certain actions. For example, the event gkEventTimerTick is sent by the TTimer module to notify subscribers that one time period has passed. To subscribe modules to the event of another module, TController offers the method
Create_Connection_Events (String idSource, String idRecipient)
This method subscribes module idRecipient to events coming from module idSource. The recipient must provide event filtering as neccessary, for example if module idSource sends out multiple types of events.
## Starting
Once everything has been created and connected we can start the network. This always happens in a predefined order - established by setting a few start entries using the method TController.Create_StartListEntry (String id) where id is the unique ID of the module to be started. Once all start entries are set we can start the network by calling TController.start (). This will start the modules in the order in which we created the start list entries.
## Stopping
When the application is finished we need to shut down the network by stopping the modules. As with the starting we need to stop modules in a predefined order, which we establish by setting entries in a stop list. A stop list entry is set by calling the method TController.Create_StopListEntry (String id) where id is the unique ID of the module to be stopped. Stopping happens automatically when the user presses CTRL-C or closes the GUI frontend.
# Events
As in any application there needs to be a measure of realtime control. ppm-java offers a simple event system which allows various modules to control aspects of the program whilst it's running.
Objects that handle events implement the interface ppm_java.typelib.IEvented. This interface provides the events used in the program as well as the method stubs to handle those (OnEvent (...)).

Event routing must be set up at the start of a ppm-java run. This is done by calling TController.Create_Connection_Events (String idSource, String idRecipient) which subscribes the object idRecipient to all events from the object idSource. It's possible to have multiple recipients for one object, and that an object can receive events from multiple sources. Having an object subscribe to multiple event sources can present problems (e.g. an object subscribing to multiple TTimers)[27].
[27] In that scenario there are ways to minimize problems, but the best way is to avoid this scenario if possible. For example, with the multiple timer scenario we might just use one timer sending gkEventTimerTick events at a high frequency which is a whole multiple of the frequency of all the TTimers we would have used and then to use frequency division and multiplexing in the object that receives the gkEventTimerTick events.
When the session runs, the source object will send events by calling one of the TController.PostEvent methods. The global TController object will pass this event on to all subscribers of the source object. This means that each subscribed recipients will receive all events emitted from the source object. It's up to each recipient to filter the events for those it's interested in.
Events are identified by plain vanilla integer constants. Normally we'd be using an enumerator or a base class for each event type. Both has disadvantages. An enumerator requires an extra import statement for each concrete implementation of IEvented, and an event class would need to be instantiated with every event fired. That's fine for the occasional event, but something like TTimer would generate many events in a short time, resulting in the creation of lots and lots of throw away event objects. And this would smell like a very silly design. Using plain-vanilla integers seemed the most economic idea, as it doesn't need any imports and does away with that crazy fabrication of throw away objects.
The OnEvent event handler is overloaded to receive one in-band parameter - as an int, a long or as a String. This is a bit cumbersome as it means that every implementation of IEvented needs to provide all overloaded versions of OnEvent[28], but the higher performance and possibility to provide in-band data is a good reason to go a bit more complex.
[28] IDE's such as Eclipse insert the resp. method stubs automatically. Text editor users have to bite the bullet, I'm afraid...
Here is a basic example of a network consisting of one event source connected to a number of receivers, each one writing to stdout on each event.
TDev_Example_Event

package ppm_java._dev.concept.example.event;

import ppm_java.backend.TController;
import ppm_java.util.logging.TLogger;

public class TDev_Example_Event
{
    public static void main (String[] args)
    {
        TLogger.CreateInstance ();	/* Otherwise NullPointerException */

        new TSource ("Source");
        new TSink ("Sink_1");
        new TSink ("Sink_2");

        TController.Create_Connection_Events ("Source", "Sink_1");
        TController.Create_Connection_Events ("Source", "Sink_2");

        TController.Create_StartListEntry ("Source");

        TController.Start ();
    }
}

TSource

package ppm_java._dev.concept.example.event;

import ppm_java.backend.TController;
import ppm_java.typelib.IControllable;
import ppm_java.typelib.IEvented;
import ppm_java.typelib.VBrowseable;

class TSource extends VBrowseable implements IEvented, IControllable
{
    public TSource (String id)
    {
        super (id);
    }

    /**
     * Sends ten events (zeros) to any subscribers.
     */
    public void Start ()
    {
        String id;
        String msg;
        int i;

        id = GetID ();
        for (i = 1; i <= 10; i++)
        {
        msg = "Event #" + i;
        TController.PostEvent (0, msg, id);
        try {Thread.sleep (1000);} catch (InterruptedException e) {}
        }
    }

    public void Stop () {/* Do nothing. */}
    public void OnEvent (int e) {/* Do nothing; this is just an event source */}
    public void OnEvent (int e, int arg0) {/* Do nothing; this is just an event source */}
    public void OnEvent (int e, long arg0) {/* Do nothing; this is just an event source */}
    public void OnEvent (int e, String arg0) {/* Do nothing; this is just an event source */}
    protected void _Register ()
    {
        TController.Register (this);
    }
}

TSink

package ppm_java._dev.concept.example.event;

import ppm_java.backend.TController;
import ppm_java.typelib.IControllable;
import ppm_java.typelib.IEvented;
import ppm_java.typelib.VBrowseable;

class TSink extends VBrowseable implements IEvented, IControllable
{
    public TSink (String id)
    {
        super (id);
    }

    public void OnEvent (int e, String arg0)
    {
        String msg;

        msg = GetID () + ": " + "Received messaging event. Message: " + arg0;
        System.out.println (msg);
    }

    public void Start () {/* Do nothing */}
    public void Stop () {/* Do nothing */}
    public void OnEvent (int e) {/* Do nothing */}
    public void OnEvent (int e, int arg0) {/* Do nothing */}
    public void OnEvent (int e, long arg0) {/* Do nothing */}
    protected void _Register ()
    {
        TController.Register (this);
    }
}

Here is the program output (stdout):
1. Sink_1: Received messaging event. Message: Event #1
2. Sink_2: Received messaging event. Message: Event #1
3. Sink_1: Received messaging event. Message: Event #2
4. Sink_2: Received messaging event. Message: Event #2
5. Sink_1: Received messaging event. Message: Event #3
6. Sink_2: Received messaging event. Message: Event #3
7. Sink_1: Received messaging event. Message: Event #4
8. Sink_2: Received messaging event. Message: Event #4
9. Sink_1: Received messaging event. Message: Event #5
10. Sink_2: Received messaging event. Message: Event #5
11. Sink_1: Received messaging event. Message: Event #6
12. Sink_2: Received messaging event. Message: Event #6
13. Sink_1: Received messaging event. Message: Event #7
14. Sink_2: Received messaging event. Message: Event #7
15. Sink_1: Received messaging event. Message: Event #8
16. Sink_2: Received messaging event. Message: Event #8
17. Sink_1: Received messaging event. Message: Event #9
18. Sink_2: Received messaging event. Message: Event #9
19. Sink_1: Received messaging event. Message: Event #10
20. Sink_2: Received messaging event. Message: Event #10
# Statistics interface
# Class hierarchy
# Roadmap
- Finish documentation (est. one week).
- True peak capabilities. So far, we just take the highest absolute sample value per GUI cycle and use that for the display. However, in reality most peaks fall between peaks on the actual waveform. This means our meter does not display the waveform peaks but only the sample peaks, resulting in an underread of typically 3dB. A truepeak module is needed to reduce the underread. We would design the truepeak module according to the recommended algorithm in BS.1770-4[29] (est one week).
  [29] BS.1770-4, Annex 2. https://www.itu.int/dms_pubrec/itu-r/rec/bs/R-REC-BS.1770-4-201510-I!!PDF-E.pdf
- Port to C++/QT. The ppm-java program is a proof of concept. And it was simply easier to do the design in Java (e.g. we don't have to keep track of header files). Once the design has matured, it should be fairly straight forward to port the program to C++, using the QT toolkit and other support libraries (est. four weeks).
# Appendices
## App. 1: Example listings

### Listing 1:

package ppm_java._dev.concept.trial.JJack;

import java.nio.FloatBuffer;
import de.gulden.framework.jjack.JJackAudioEvent;
import de.gulden.framework.jjack.JJackAudioProcessor;
import de.gulden.framework.jjack.JJackException;
import de.gulden.framework.jjack.JJackSystem;
import ppm_java.util.logging.TLogger;

/**
 * Loads the JJack driver, connects to a running instance of JackD and prints
 * the peak of every incoming frame to stdout.
 *
 * @author peter
 */
public class TDev_Trial_JJack_process_01 implements JJackAudioProcessor
{
    public static void main (String[] args)
    {
        TDev_Trial_JJack_process_01 processor;

        /* Setting up Jack client and terminator thread. */
        processor = new TDev_Trial_JJack_process_01 ();

        /* Connecting with the running instance of Jack */
        JJackSystem.setProcessor (processor);

        /* Terminator timer - must run in separate thread */
        new Thread ()
        {
        public void run ()
        {
        try
        {
        Thread.sleep (500);
        JJackSystem.shutdown ();
        }
        catch (JJackException | InterruptedException e)
        {
        e.printStackTrace();
        }
        System.exit (1);
        }
        }.start ();
    }

    private int fIFrame;

    public TDev_Trial_JJack_process_01 ()
    {
        fIFrame = 0;
    }

    /**
     * The process callback. Called by the Jack server via the JJack bridge. Time critical!
     */
    @Override
    public void process (JJackAudioEvent e)
    {
        FloatBuffer inBuf;
        int nSamples;
        int i;
        float s;
        float sRect;
        float peak;

        fIFrame++;
        inBuf = e.getInput (0);
        nSamples = inBuf.limit ();
        peak = 0;
        for (i = 0; i < nSamples; i++)
        {
        /* Get next sample. */
        s = inBuf.get (i);

        /* Rectify (i.e. mirror a negative sample to it's positive opposite). */
        sRect = (s < 0) ? -s : s;

        /* Determine peak value. */
        peak = (sRect > peak) ? sRect : peak;
        }
        System.out.println ("Frame: " + fIFrame + "; Peak value (abs): " + peak + ".");
    }
}

## Glossary
Critical section
In concurrent programming, concurrent accesses to shared resources can lead to unexpected or erroneous behavior, so parts of the program where the shared resource is accessed is protected. This protected section is the critical section or critical region. It cannot be executed by more than one process. Typically, the critical section accesses a shared resource, such as a data structure, a peripheral device, or a network connection, that would not operate correctly in the context of multiple concurrent accesses.
https://en.wikipedia.org/wiki/Critical_section
Priority inversion
In computer science, priority inversion is a problematic scenario in scheduling in which a high priority task is indirectly preempted by a lower priority task effectively "inverting" the relative priorities of the two tasks.
This violates the priority model that high priority tasks can only be prevented from running by higher priority tasks and briefly by low priority tasks which will quickly complete their use of a resource shared by the high and low priority tasks.
https://en.wikipedia.org/wiki/Priority_inversion
# License
A program to display audio levels using PPM ballistics.
Copyright (C) 2017 Peter Hoppe
This program is free software: you can redistribute it and/or modify it under the terms of the GNU General Public License as published by the Free Software Foundation, either version 3 of the License, or (at your option) any later version.
This program is distributed in the hope that it will be useful, but WITHOUT ANY WARRANTY; without even the implied warranty of MERCHANTABILITY or FITNESS FOR A PARTICULAR PURPOSE. See the GNU General Public License for more details.
You should have received a copy of the GNU General Public License along with this program. If not, see <http://www.gnu.org/licenses/>.